## Slide 1
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Retail interior / coordinated design
Design intent, measured geometry and assembly strategies
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-01
PROJECT
2400 × 3106 internal
2600 ceiling
Black steel / plaster / stone-look floor
ISSUE PURPOSE
Client review and consultant coordination. Detailed strategies are preliminary pending the stated confirmations.
DRAWING PRIORITY
Geometry follows approved Rev A. Render conveys material and lighting character only.
READING SEQUENCE
Layout → elevations → materials → assembly details → coordination decisions.
REFERENCE RENDER · NOT TO SCALE · styling props excluded from technical scope

## Slide 2
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Drawing basis / document hierarchy
Confirmed design, assumed site conditions and fabrication decisions
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-02
SOURCE PDF
Repository presentation.pdf, 10 pages. Reorganised and redrawn into an A3 landscape architectural package.
SOURCE LIMIT
Named reference books were not supplied. No page-specific technical claims or citations are made.
ISSUE STATUS
Final presentation file; preliminary technical details. Not a fabrication or compliance approval.
D
CONFIRMED DESIGN
Black geometry / blue dimensions. Owner-confirmed Rev A, including four 664 modules and the centred counter.
S
SITE ASSUMPTION
Red clouds #4, #23, #26. No dimensions have been independently surveyed. Internal finish faces and FFL require survey.
F
FABRICATION PROPOSAL
Red clouds #16 / #26. Detail geometry, tolerances and products require consultant and fabricator confirmation.
TBC #16 / #26 — no structural capacities, glass certifications or anchor schedules are inferred.

## Slide 3
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Overall plan / setting-out
AP-03 · front-left internal origin; x across, y into shop
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-03
01 / ENVELOPE
2400 × 3106 clear finished dimensions assumed. Verify finished faces before fabrication (#4).
02 / COUNTER
1000 × 450 × 900H
x = 700–1700
y = 1706–2156
03 / ACCESS CHECK
450 on either side of counter. These do not meet the project’s assumed 900 route. Consultant decision #16 required.
04 / REAR CONNECTION
Side units continue to rear wall. Rear bays occupy x=250–750 and 1650–2150; no footprint overlap.
2400
3106
450
450
700
COUNTER
REAR
0 2000 mm | 1:20
#16 — 450 SIDE GAPS
Escape / staff access unresolved
N ↓ storefront
ASSUMED #23

## Slide 4
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Floor finish / module setting-out
AP-04 · porcelain extent includes floor beneath units
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-04
M04 / PORCELAIN
1200 × 600 rectified stone-look porcelain. Option A: long side across shop. Joint = 2; perimeter = 5.
WIDTH CHAIN
5 + 1194 + 2 + 1194 + 5 = 2400
DEPTH CHAIN
5 + 343 + (4 × 600) + (5 × 2) + 343 + 5 = 3106
FLOOR BUILD-UP
Tile, adhesive and substrate thicknesses TBC #26. Flush threshold detail on AP-17; no step introduced.
2400
3106
1194
343
0 2000 mm | 1:20
#4 / #26
Survey before tile ordering.
Cuts exclude fabrication tolerances.

## Slide 5
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Ceiling / lighting coordination
AP-05 · lighting positions follow confirmed Rev A
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-05
L01 / TRACKS
Two black tracks: x=650 / 1750, y=450–2656. Four adjustable cylindrical spots per track. All lighting 3000 K.
L02 / DOWNLIGHTS
Three fittings at x=700 / 1200 / 1700; y=225. Spacing retained from approved design.
L03 / SHELF + PLINTH
Concealed under-shelf LEDs; toe-kick LEDs 2 × 2656. Access and wiring strategy AP-14.
CEILING / MEP
Smooth gypsum, warm off-white. Ceiling support, fire/MEP devices and driver ventilation require consultant coordination #16.
2400
3106
2206
0 2000 mm | 1:20

## Slide 6
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Storefront / external elevation
AP-06 · glazed entrance and halo-lit fascia
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-06
FRONTAGE
450 + 1500 + 450 = 2400. The 450 × 450 display columns face the street; shelf depth remains 250.
G01 / GLAZING
Door 1000 × 2580 × 12 toughened glass. Fixed pane 488 W. Three nominal 4 gaps: 488 + 1000 + 12 = 1500.
SIGN BAND
600 high above 2600 ceiling datum; total storefront height 3200. Exterior logo 1000 W, uniformly scaled.
DETAIL REFERENCES
Head AP-15
Jamb / pivot AP-16
Flush threshold AP-17
Sign backing AP-18
2400
3200
2580
600
12 mm GLASS
0 2000 mm | 1:20
#16 — top/bottom clearance
10 + 2580 + 10 = 2600
PROPOSED split; glazier to confirm

## Slide 7
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Rear focal wall / internal elevation
AP-07 · wall-mounted non-illuminated brand mark
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-07
REAR MODULES
250 side + 500 display + 900 logo zone + 500 display + 250 side = 2400. Rear display depth 250.
BRAND
600 W logo at centre z=1900. Native asset ratio retained; approximately 271.8 H. No illumination or rear mesh.
DISPLAY LEVELS
600 / 1000 / 1400 / 1800 / 2200 AFFL. Frame 2600; top mesh is confined to side units.
ASSEMBLY
Removable central back panel and wall fixing strategy AP-19. Rear shelf LEDs return into accessible service routes.
2400
2600
900
0 2000 mm | 1:20

## Slide 8
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Left display / internal elevation
Full side run retained; rear units fit between side footprints
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-08
FOUR MODULES
450 storefront + 4 × 664 = 3106. Module boundaries at 450 / 1114 / 1778 / 2442 / 3106.
VERTICAL SCHEDULE
100 plinth + 500 cabinet + 5 × 400 = 2600. Display decks at 600 to 2200.
MESH / DOORS
Mesh zone 2200–2600 on front plane. Doors 1.5 mm steel, flush handleless, light-neutral PPC.
FABRICATION HOLD
664 is a design module, not a shelf cutting size. Shared posts, welds, coatings and adjustment affect clear spans. See AP-12.
3106
2600
664
664
664
664
STOREFRONT
REAR
0 2000 mm | 1:20

## Slide 9
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Right display / internal elevation
Full side run retained; rear units fit between side footprints
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-09
FOUR MODULES
450 storefront + 4 × 664 = 3106. Module boundaries at 450 / 1114 / 1778 / 2442 / 3106.
VERTICAL SCHEDULE
100 plinth + 500 cabinet + 5 × 400 = 2600. Display decks at 600 to 2200.
MESH / DOORS
Mesh zone 2200–2600 on front plane. Doors 1.5 mm steel, flush handleless, light-neutral PPC.
FABRICATION HOLD
664 is a design module, not a shelf cutting size. Shared posts, welds, coatings and adjustment affect clear spans. See AP-12.
3106
2600
664
664
664
664
REAR
STOREFRONT
0 2000 mm | 1:20

## Slide 10
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Spatial assembly / cutaway axonometric
AP-10 · generated from approved coordinates; parallel projection
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-10
SPATIAL LOGIC
Four side modules on each wall; rear bays sit between side-unit faces. Storefront columns turn toward the street.
COUNTER
Centred counter retained. Side access conflicts remain visible in plan AP-03 and in the decision register.
MODEL LIMIT
Diagrammatic cutaway. Wall thickness, fixings and glass hardware are not inferred from the render.
MATERIAL LANGUAGE
Black steel structure; neutral cabinets; plaster backdrop; continuous porcelain floor. No loose products or styling props.
Axonometric geometry is independent of the AI render. View is not a measurement source.

## Slide 11
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Material palette / visible finishes
AP-11 · sample-led specification; colours are indicative
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-11
M01 / BLACK STEEL
25 × 25 × 1.6 main SHS
20 × 20 × 1.6 secondary SHS
Matte black powder coat
M02 / CABINET STEEL
1.5 mm PPC doors
Light-neutral finish
Flush, handleless
M03 / PLASTER
Raw light textured plaster
Approve physical sample
Substrate / buildup #26
M04 / PORCELAIN
1200 × 600 rectified
2 grout / 5 perimeter joint
Stone-look, sample approval
G01 / CLEAR GLASS
12 mm toughened door
Hardware / gaps #16
Fixed pane specification TBC
M05 / EXPANDED MESH
Approx. 20 × 40 diamond
Black finish / framed edges
Gauge and fixing #16

## Slide 12
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Display module / fabrication logic
AP-12 · typical module and installation sequence
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:10 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-12
MODULE ≠ CUT SIZE
664 is the module allocation. Shared 25 posts are centred at internal boundaries; end posts are inside run ends.
UPRIGHT CENTRES
y=462.5 / 1114 / 1778 / 2442 / 3093.5. Clear spans: 626.5 / 639 / 639 / 626.5 before fit allowances.
WORKSHOP
Weld frames on jigs; deburr; prepare and coat. Confirm weld size, distortion allowance and coating buildup #16.
SITE
Survey → dry fit → level/adjust → anchor to verified floor/wall → connect services → fit removable trays and mesh. No gypsum anchorage.
664
1200
LOWER MODULE / UPPER ZONE CONTINUES
PROPOSED #16
Drawing shows an isolated module.
Do not copy 614 clear to shared-post bays.
Shelf fit clearance and frame segmentation require fabricator approval.
Full elevation: AP-08 / AP-09.

## Slide 13
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Shelf / frame / concealed LED
AP-13 · section through 250-deep display shelf
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:2 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-13
CONFIRMED
3 mm folded MS tray. 25 front downstand. 250 total shelf projection. 20 × 20 × 1.6 support SHS.
LIGHTING STRATEGY
Removable aluminium LED channel beneath tray; diffuser screened by downstand. 3000 K. Profile, setback and wattage TBC #16.
SERVICE ACCESS
Tray/channel accessible from below. Concealed cable follows rear upright with protected holes, grommets and strain relief.
LOAD / FIT
Shelf loading, span deflection, welds, fasteners and actual LED housing dimensions require fabricator/consultant confirmation.
250
25
TBC #16 — LED housing drawn as an indicative envelope. Confirm housing, fixing and setback against the selected product. No drilling schedule released.
01 TRAY + DOWNSTAND 02 SUPPORT SHS 03 REMOVABLE LED CHANNEL
02 / 20 SHS support
01 / 25 downstand
03 / diffuser + cable

## Slide 14
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Mesh / lighting / service access
AP-14 · removable components and segregated service routes
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:5 / NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-14
MESH PANEL
2200–2600 front infill only. Approx. 20 × 40 diamond mesh; gauge, strand width and open area TBC #16.
EDGE / REMOVAL
Capture cut mesh edges in removable perimeter frame. Screw-fix accessible panel to main structure; no sharp exposed edges.
LED DRIVERS
Locate in accessible ventilated cabinet service zone. Keep maintenance reachable without dismantling the display.
ELECTRICAL
Separate mains/data/low-voltage routes as required by consultant. Driver rating, cable sizes, ventilation and circuits remain #16.
664
400
TBC #16 — PANEL + SERVICE STRATEGY
Workshop-welded steel subframe → deburr and coat → demountable mesh cassette.
Accessible mains isolation → ventilated driver zone → protected LV route in upright → shelf channels.
Fixing centres, panel gauge and ventilation area are unapproved. Diagram is not a product specification.

## Slide 15
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Storefront head / structural interface
AP-15 · glazing head and pivot reinforcement strategy
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:2 — indicative assembly @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-15
DOOR HEIGHT
2580 door within 2600 opening leaves 20 total vertical allowance. Propose 10 top / 10 bottom; glazier to confirm #16.
LOAD PATH
Top pivot fixed to engineered steel support tied to verified structure. Plaster / gypsum and fascia are not structural supports.
FASCIA ACCESS
Removable internal access panel for pivot inspection and sign driver. Panel size and backing construction TBC #16/#26.
GLASS RELEASE
Confirm door mass, hardware capacity, deflection limits, hole positions and approved glass fabrication drawings before cutting.
12 glass
VERIFIED STRUCTURE — TYPE / DEPTH TBC
Pivot to reinforced head
Accessible support / fixings
TBC #16 / #26 — reinforcement, pivot housing and substrate shown diagrammatically. No anchor size or structural capacity specified. Head detail coordinates with AP-16 / AP-17.

## Slide 16
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Glazed entrance / jamb and pivot
AP-16 · horizontal joint chain and operation envelope
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:5 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-16
WIDTH CHAIN
4 + 488 + 4 + 1000 + 4 = 1500. Nominal gaps are design allowances, not approved glass fabrication dimensions.
PIVOT
100 from right door edge, viewed externally. Inward opening. Long-side sweep radius 900; short tail radius 100.
SEALS / EDGES
Compatible removable gaskets, setting blocks and edge protection. Seal thickness and compression to glazier details #16.
COORDINATION
Confirm effective clear opening, short-tail sweep, handles and stops. 1000 leaf width does not certify a 1000 clear escape opening.
488
4 gap
FIXED PANE → DOOR JUNCTION / PARTIAL LEAF
100
PIVOT ZONE / RIGHT EDGE
TBC #16 — supplier to resolve pane edge support, seal pockets, pivot footprint and operating clearances before glass order.

## Slide 17
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Flush threshold / floor interface
AP-17 · accessible level transition and recessed hardware
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:2 — indicative assembly @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-17
DESIGN LEVEL
No step or raised sill. Internal and external finished surfaces meet flush; external levels require survey #26.
FLOOR PIVOT
Recessed pivot/closer supported by verified structural substrate. Independent of tile and adhesive; removable cover flush with FFL.
MOVEMENT / SEAL
Maintain 5 perimeter movement allowance where applicable. Compatible flexible seals; do not bridge joints with rigid grout.
SITE CONFIRMATION
Slab depth, services, damp protection and external drainage must be verified before recessing hardware or setting threshold level.
FFL ±0 — VERIFY ON SITE #26
RECESSED HARDWARE ENVELOPE TBC
Independent structural support
12 glass / seal TBC #16
TBC #16 / #26 — tile/adhesive/slab thicknesses and hardware pocket are indicative. Preserve the flush finished level; coordinate seals and maintenance access.

## Slide 18
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Halo-lit sign / demountable backing
AP-18 · external logo section and maintenance access
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:2 — indicative assembly @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-18
BRAND / FINISH
1000 W black logo; uniform native SVG geometry. Halo-lit, 3000 K visual intent. No brass elements.
STAND-OFF
25 stand-off behind logo. Concealed threaded spacers to engineered backing; fastener size and count remain #16.
POWER / ACCESS
Protected cable penetration to accessible driver on removable internal backing panel. Strain relief and isolation accessible.
FABRICATION
Confirm return depth, LED spacing, weather exposure, fixing template, driver enclosure and backing capacity with sign specialist.
25 stand-off
STRUCTURAL BACKING / ACCESS PANEL TBC
Threaded spacer / concealed stud
Protected wire to accessible driver
Removable backing panel
TBC #16 / #26 — backing thickness and logo return depth are indicative. Show a removable driver-access panel; do not permanently seal the service compartment.

## Slide 19
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Rear wall / display-to-wall connection
AP-19 · maintainable back-panel and service junction
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:5 — indicative assembly @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-19
CENTRAL ZONE
900 design zone, 875 clear between shared 25 uprights. 600 logo leaves 137.5 each side within that clear width.
NON-ILLUMINATED
Rear logo remains black and non-illuminated. Cable routes serve adjacent shelf LEDs only.
WALL FIXING
Floor/wall-fixed structure. Adjustable brackets to verified substrate; isolate finish from structural fixings.
MAINTENANCE
Removable central light-neutral metal panel on accessible clips/screws. Panel gauge, fasteners and reveals TBC #16/#26.
900
TBC #16 / #26 — this is a partial-height panel strategy. Confirm actual panel extent, reveal and wall finish build-up. Separate demountable metal from plaster; no load transfer to gypsum ceiling.

## Slide 20
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Counter / plan, elevation and section
AP-20 · 1000 × 450 × 900H retained
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:10 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-20
1000
450
01 PLAN — 1000 × 450
1000
900
02 FRONT ELEVATION
450
03 SECTION
TBC #16 / #26 — counter interior is a proposed arrangement: 20 top, steel carcass/frame, removable storage trays, rear service chase and adjustable feet. Confirm all new thicknesses, storage layout, service clearances and feet before fabrication. External 1000 × 450 × 900 and 300 × 450 mesh insert remain confirmed.

## Slide 21
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Counter / services and removable access
AP-21 · section through proposed service compartment
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:5 — indicative assembly @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-21
TOP / FRONT
Simple light-coloured top; light-neutral steel front. Proposed 20 solid-surface top on steel support; material/thickness approval #16.
STORAGE
Removable steel trays/drawers, avoiding timber or heavy joinery. Slide specification, payload and usable depth TBC #16.
POWER / DATA
Proposed rear grommet to segregated service chase; accessible isolation and removable panel on staff side.
LEVELLING
Concealed adjustable feet bear on verified floor. Finish to remain at 900H. Foot travel and point loads require consultant confirmation.
450
900
TBC #16 / #26
Internal dimensions are proposed.
Confirm selected grommet, service chase, drawer slides and feet.
Staff access remains a separate open issue.

## Slide 22
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Finish junctions / controlled terminations
AP-22 · four typical coordination details
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:2 — indicative assemblies @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-22
01 FLOOR / WALL
02 WALL / CEILING
03 DISPLAY / WALL
04 INTERNAL CORNER
5 joint
Flexible compatible seal
Build-up TBC
Controlled reveal TBC
Independent ceiling support
Adjustable wall bracket
Accessible fastener / packer
Plan / internal return
Reinforced plaster corner
Movement treatment TBC
TBC #16 / #26 — all build-ups and bracket/reveal geometries shown provisionally. Retain the confirmed 5 floor perimeter allowance. Confirm movement, substrate, finish stops, fixing capacity and visible sample before construction.

## Slide 23
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Technical specification / coordinated schedule
AP-23 · performance decisions remain with the responsible specialists
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-23
CODE
ASSEMBLY
DESIGN BASIS
CONFIRM BEFORE FABRICATION
M01
Main / secondary steel
25×25×1.6 / 20×20×1.6 SHS; matte black PPC
Weld/anchor design, corrosion prep and loading #16
M02
Doors / neutral panels
1.5 mm PPC steel doors; flush, handleless
Hardware, reveals and durability sample #16
M03
Wall / ceiling
Raw light plaster; smooth off-white gypsum ceiling
Substrate, thickness and fire requirements #26/#16
M04
Floor / sealants
1200×600 porcelain; 2 grout; 5 perimeter
Adhesive, slip suitability, sealant compatibility #16/#26
G01
Glazing / hardware
1000×2580×12 toughened pivot leaf; 488 fixed pane
Fixed pane thickness, gaps, hardware capacity #16
M05
Mesh
Approx. 20×40 diamond; black; framed removable edges
Gauge, perimeter channel and screw centres #16
M06
Shelf
3 mm MS tray; 25 downstand; 250 deep
Load, tray fit and LED extrusion selection #16
L01
Lighting / access
3000 K; two tracks; shelf and plinth LEDs
Photometry, wattage, drivers, circuits, ventilation #16
S01
Logo / fixings
External halo-lit at 25 stand-off; internal unlit
Backing, studs, maintenance opening and IP needs #16
C01
Counter / joints
1000×450×900; 300×450 mesh; light top
Proposed 20 top, storage, feet, grommet, reveals #16

## Slide 24
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Installation / quality and maintenance sequence
AP-24 · hold points before release to fabrication
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-24
01 / SURVEY
Confirm finished envelope, FFL, substrate, wall construction and site north. Record measured values separately from design dimensions.
02 / CONSULTANT
Resolve 450 side routes; assess pivot clear opening, fire / MEP coordination, structure and fixing loads. Sign off TBC #16.
03 / SHOP DRAWINGS
Fabricator resolves cut sizes, shared posts, welds, glass gaps, tolerances and adjustment. Release supplier templates only after approval.
04 / SAMPLE + FABRICATE
Approve finishes, edge conditions and light concealment. Workshop weld and coat; protect completed finishes during transport.
05 / SITE ASSEMBLY
Set out → level → anchor to verified structure → route/test services → install trays, panels, glass and logo → adjust and protect.
06 / COMMISSION
Test door sweep, access, lighting and isolation. Demonstrate panel removal; hand over wiring, maintenance instructions and surveyed as-builts.

## Slide 25
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Open decisions / consultant coordination
AP-25 · retain clouds until documented approval
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-25
#4 FINISHED ENVELOPE / Surveyor / owner
Survey 2400 × 3106 after plaster; check diagonals, plumb and ceiling height.
#16 COUNTER / ESCAPE / Fire / access consultant
450 side gaps vs 900 project assumption. Confirm compliant staff/customer route; retain centred design pending decision.
#16 GLASS / HARDWARE / Glazier / engineer
2580 door height leaves 20 vertical allowance. Confirm split, fixed-pane thickness, operating gaps and pivot capacity.
#16 SERVICES / FIXINGS / MEP / structural / fabricator
No anchor capacities, lighting circuits or driver ventilation established. Review proposed AP-13 to AP-22 assemblies.
#23 ORIENTATION / Surveyor
North toward storefront is assumed. No surveyed north is represented in this package.
#26 WALL / DATUM / FINISHES / Surveyor / architect
100 wall is historical assumption; plans show finish lines only. Verify wall/ceiling/floor build-ups, levels and movement joints.

## Slide 26
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Drawing register / dimensional close-out
AP-26 · presentation consistency audit and next release
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-26
SHEET REGISTER
AP-01 Retail interior / coordinated design
AP-02 Drawing basis / document hierarchy
AP-03 Overall plan / setting-out
AP-04 Floor finish / module setting-out
AP-05 Ceiling / lighting coordination
AP-06 Storefront / external elevation
AP-07 Rear focal wall / internal elevation
AP-08 Left display / internal elevation
AP-09 Right display / internal elevation
AP-10 Spatial assembly / cutaway axonometric
AP-11 Material palette / visible finishes
AP-12 Display module / fabrication logic
AP-13 Shelf / frame / concealed LED
AP-14 Mesh / lighting / service access
AP-15 Storefront head / structural interface
AP-16 Glazed entrance / jamb and pivot
AP-17 Flush threshold / floor interface
AP-18 Halo-lit sign / demountable backing
AP-19 Rear wall / display-to-wall connection
AP-20 Counter / plan, elevation and section
AP-21 Counter / services and removable access
AP-22 Finish junctions / controlled terminations
AP-23 Technical specification / coordinated schedule
AP-24 Installation / quality and maintenance sequence
AP-25 Open decisions / consultant coordination
AP-26 Drawing register / dimensional close-out
CHECKED: 450 + 1500 + 450 = 2400 | 488 + 1000 + 3×4 = 1500 | 450 + 4×664 = 3106
100 + 500 + 5×400 = 2600 | 3106 − 250 − 2156 = 700 | counter 1000×450×900
Surveys and fabrication decisions remain open. Detailed read-back audit accompanies this presentation.