## Slide 1
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Retail interior / coordinated design
Design intent, measured geometry and assembly strategies
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-01
PROJECT
2400 × 3106 internal
2600 ceiling
Black steel / plaster / stone-look floor
ISSUE PURPOSE
Client review and consultant coordination. Detailed strategies are preliminary pending the stated confirmations.
DRAWING PRIORITY
Geometry follows approved Rev A. Render conveys material and lighting character only.
READING SEQUENCE
Layout → elevations → materials → assembly details → coordination decisions.
REFERENCE RENDER · NOT TO SCALE · styling props excluded from technical scope

## Slide 2
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Overall plan / setting-out
Setting-out / coordinated interfaces · 1:20 · finish-face dimensions; site verification pending
FOR COORDINATION · SITE ITEMS OPEN · REV C 06 OCT 2026 / SOURCE REV A
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-03
01 / FRAME + SETTING-OUT
250 deep side units. Four 664 modules from y=450 to 3106. 25 main uprights shown; shelf/support lines distinguished.
02 / COUNTER + REAR
1000 × 450 counter; x=700–1700, y=1706–2156. 700 to rear-unit face. Side routes remain 450 / 450.
03 / GLAZED ENTRANCE
488 fixed pane + 1000 pivot leaf + three 4 gaps = 1500. Pivot 100 from right edge; inward sweep shown.
04 / COORDINATION STATUS
LOD 350 development target: interfaces shown, not certified complete. Anchors, hardware, substrate and access remain TBC #16/#26.
2400
450
1500
450
3106
450
664
664
664
664
250
1900
250
450
450
700
A
B
C
D
01
02
03
SET-OUT DATUMS
A 0 / 0
B 2400 / 0
C 2400 / 3106
D 0 / 3106
#16
450 side routes
Access / escape unresolved
N ↓ STOREFRONT
ASSUMED #23
Wall bands graphic only
Thickness TBC #26
Envelope TBC #4
0 1000 mm | 1:20

## Slide 3
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Floor finish / module setting-out
AP-04 · porcelain extent includes floor beneath units
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-04
M04 / PORCELAIN
1200 × 600 rectified stone-look porcelain. Option A: long side across shop. Joint = 2; perimeter = 5.
WIDTH CHAIN
5 + 1194 + 2 + 1194 + 5 = 2400
DEPTH CHAIN
5 + 343 + (4 × 600) + (5 × 2) + 343 + 5 = 3106
FLOOR BUILD-UP
Tile, adhesive and substrate thicknesses TBC #26. Flush threshold detail on AP-17; no step introduced.
2400
3106
1194
343
0 2000 mm | 1:20
#4 / #26
Survey before tile ordering.
Cuts exclude fabrication tolerances.

## Slide 4
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Ceiling / lighting coordination
AP-05 · lighting positions follow confirmed Rev A
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-05
L01 / TRACKS
Two black tracks: x=650 / 1750, y=450–2656. Four adjustable cylindrical spots per track. All lighting 3000 K.
L02 / DOWNLIGHTS
Three fittings at x=700 / 1200 / 1700; y=225. Spacing retained from approved design.
L03 / SHELF + PLINTH
Concealed under-shelf LEDs; toe-kick LEDs 2 × 2656. Access and wiring strategy AP-14.
CEILING / MEP
Smooth gypsum, warm off-white. Ceiling support, fire/MEP devices and driver ventilation require consultant coordination #16.
2400
3106
2206
0 2000 mm | 1:20

## Slide 5
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Storefront / external elevation
AP-06 · glazed entrance and halo-lit fascia
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-06
FRONTAGE
450 + 1500 + 450 = 2400. The 450 × 450 display columns face the street; shelf depth remains 250.
G01 / GLAZING
Door 1000 × 2580 × 12 toughened glass. Fixed pane 488 W. Three nominal 4 gaps: 488 + 1000 + 12 = 1500.
SIGN BAND
600 high above 2600 ceiling datum; total storefront height 3200. Exterior logo 1000 W, uniformly scaled.
DETAIL REFERENCES
Head AP-15
Jamb / pivot AP-16
Flush threshold AP-17
Sign backing AP-18
2400
3200
2580
600
12 mm GLASS
0 2000 mm | 1:20
#16 — top/bottom clearance
10 + 2580 + 10 = 2600
PROPOSED split; glazier to confirm

## Slide 6
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Rear focal wall / internal elevation
AP-07 · wall-mounted non-illuminated brand mark
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-07
REAR MODULES
250 side + 500 display + 900 logo zone + 500 display + 250 side = 2400. Rear display depth 250.
BRAND
600 W logo at centre z=1900. Native asset ratio retained; approximately 271.8 H. No illumination or rear mesh.
DISPLAY LEVELS
600 / 1000 / 1400 / 1800 / 2200 AFFL. Frame 2600; top mesh is confined to side units.
ASSEMBLY
Removable central back panel and wall fixing strategy AP-19. Rear shelf LEDs return into accessible service routes.
2400
2600
900
0 2000 mm | 1:20

## Slide 7
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Left display / internal elevation
Developed display elevation · interfaces + material codes · bottles indicative only
FOR COORDINATION · SITE ITEMS OPEN · REV C 06 OCT 2026 / SOURCE REV A
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-08
01 / STEEL FRAME
25 × 25 × 1.6 main SHS; 20 × 20 × 1.6 secondary supports. 664 module is not a fabrication cut size.
02 / SHELF + LIGHT
3 mm tray / 25 downstand / 250 depth. Concealed 3000 K LED behind front edge; see section inset.
03 / BASE + MESH
600 base includes 100 recessed plinth. 1.5 PPC doors. Mesh at 2200–2600; approximate 20 × 40 diamonds.
04 / INDICATIVE CONTENT
Sparse fragrance bottles added at owner request for visual scale only. Excluded from dimensions and schedules. Fixings and cable routing #16 remain open.
3106
2600
664
664
664
664
100
500
400
400
400
400
400
03
02
01
M01 / BLACK STEEL M02 / NEUTRAL PPC M05 / MESH L03 / 3000 K LED
250
SHELF SECTION 1:5
0 1000 mm | 1:20
INDICATIVE BOTTLES · NOT A STOCK / CAPACITY SCHEDULE

## Slide 8
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Right display / internal elevation
Developed display elevation · interfaces + material codes · bottles indicative only
FOR COORDINATION · SITE ITEMS OPEN · REV C 06 OCT 2026 / SOURCE REV A
06 OCT 2026 / SOURCE REV A
1:20 @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-09
01 / STEEL FRAME
25 × 25 × 1.6 main SHS; 20 × 20 × 1.6 secondary supports. 664 module is not a fabrication cut size.
02 / SHELF + LIGHT
3 mm tray / 25 downstand / 250 depth. Concealed 3000 K LED behind front edge; see section inset.
03 / BASE + MESH
600 base includes 100 recessed plinth. 1.5 PPC doors. Mesh at 2200–2600; approximate 20 × 40 diamonds.
04 / INDICATIVE CONTENT
Sparse fragrance bottles added at owner request for visual scale only. Excluded from dimensions and schedules. Fixings and cable routing #16 remain open.
3106
2600
664
664
664
664
100
500
400
400
400
400
400
03
02
01
M01 / BLACK STEEL M02 / NEUTRAL PPC M05 / MESH L03 / 3000 K LED
250
SHELF SECTION 1:5
0 1000 mm | 1:20
INDICATIVE BOTTLES · NOT A STOCK / CAPACITY SCHEDULE

## Slide 9
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Spatial assembly / cutaway axonometric
Shaded cutaway / approved geometry + render material language · near wall and ceiling removed
FOR COORDINATION · SITE ITEMS OPEN · REV C 06 OCT 2026 / SOURCE REV A
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-10
01 / SPATIAL CHARACTER
Warm plaster, black frames, mesh, neutral cabinetry and warm shelf lighting follow the reference render.
02 / GEOMETRIC BASIS
2400 × 3106 × 2600 envelope. Four 664 modules; centred 1000 × 450 counter; 500 / 900 / 500 rear zones.
03 / CUTAWAY
Near-side upper units and ceiling removed to expose the room. Their full extent remains on the plans and elevations.
04 / ACCURACY LIMIT
Visual fidelity target, not a measurable 80% certification. Approved dimensions override the render. Bottles are indicative; hardware and fixings remain TBC.
CUTAWAY AXONOMETRIC · NTS · ceiling and near-side upper joinery omitted

## Slide 10
BORN FRAGRANCE / ARCHITECTURE + INTERIOR DESIGN
Material palette / visible finishes
AP-11 · sample-led specification; colours are indicative
FOR COORDINATION · SITE ITEMS OPEN · REV B
06 OCT 2026 / SOURCE REV A
NTS @ A3 · DIMENSIONS mm
SPEC SNAPSHOT eeccbde1cd
AP-11
M01 / BLACK STEEL
25 × 25 × 1.6 main SHS
20 × 20 × 1.6 secondary SHS
Matte black powder coat
M02 / CABINET STEEL
1.5 mm PPC doors
Light-neutral finish
Flush, handleless
M03 / PLASTER
Raw light textured plaster
Approve physical sample
Substrate / buildup #26
M04 / PORCELAIN
1200 × 600 rectified
2 grout / 5 perimeter joint
Stone-look, sample approval
G01 / CLEAR GLASS
12 mm toughened door
Hardware / gaps #16
Fixed pane specification TBC
M05 / EXPANDED MESH
Approx. 20 × 40 diamond
Black finish / framed edges
Gauge and fixing #16